## Slide 1
CSCI 233 Internet Protocols Class 6
Dave Roberts

## Slide 2: Key Principles
Good citizen principle
Conserve router time
End-to-end operation

## Slide 3: Agenda
Routing Architecture
  Cores, peers and algorithms
Autonomous Systems
  Routing between autonomous systems

## Slide 4: Origin of Routing Tables
Routers interconnect networks
Datagram travels from router to router until it reaches a router attached to the same network as the final destination—then it gets delivered using the local network
Routing table has network id, address of next machine for that network id
How does the routing table get its information?
How is the routing table maintained?
Does the routing table have the MAC address or the IP address of the next machine?

## Slide 5: Routers and Hosts
Host may have only 2 routes
  Route for local network
  Default route to local router
Interstate road sign analogy—successive signs on 270 headed south toward Potomac
  Right to Gaithersburg
  Right to Rockville
  Right to Potomac
Interstate road signs don’t list all destinations
Still give complete directions
Signs analogous to routing tables

## Slide 6: Road Analogy
Possible configurations:
Star configuration of roads, single central intersection—say, at town square. Signs at square must show routes to all destinations.
Roads a richly connected network, signs at every intersection to all destinations.
Two towns, separated by bridge over river. Neither trusts the other, so signs on West for destinations on Western side, signs on East for destinations on Eastern side of river
Notes: Star configuration won’t work because of the requirement for a centralized switch, with capacity requirements that would make it the largest machine in the system, growing literally without limit.
Richly connected network won’t do, because there are too many street signs to maintain correctly.
Third approach is the real analogy to the Internet. Router is the bridge, router table just says “if it’s on the other side, cross the bridge.”

## Slide 7: Cores
Original Internet architecture
Use central core routers with complete information, outer routers with partial information
Job of local administrators is simplified
Potential for inconsistency, which can make some outlying destinations unreachable

## Slide 8: Core Routers
Early Internet used Arpanet as backbone. Every site had to advertise Internet addresses
All nonlocal traffic was passed to the closest core router.

## Slide 9: Core Router Problem
This approach doesn’t work if core routers have incomplete information. If destination is unknown, default route is to core router. Then core router default path can pass through all other routers if core router doesn’t know the route to it .
Potential for large number of router hops for a datagram that takes the default path.

## Slide 10: Core Router Problem…Solved
Core routers exchanged routing information so that each had complete information about optimal routes to all destinations
What’s wrong with this picture:
Internet outgrew any possible central backbone
Not every site had could have a core router
Core router interaction limits ultimate scalability
Notes: Q--What would core router do if it did not have a destination to the specified destination address for a datagram?
A—Send ICMP message. Which ICMP message? Destination unreachable.

## Slide 11: Peer Backbones—More Complexity
NFSNet backbone, when it became a peer backbone, introduced more complexity.
Very complex for core routers to know optimal routes to all hosts. Easy for illegal address to cause router loop.
Notes: If hosts on left are on west coast, hosts on right are on east, how to route from 1 to 4? Go over Arpanet backbone to R3 then to NSFNet backbone to host 4? Or take R1 to NSFNet backbone, then NSFNet backbone to host 4? Answer depends on capacity and utilization of routers, networks.
For peer networks, routing tables need different routes for different hosts, cannot route all datagrams for hosts on another network through the same router.
If routes are not consistent between the two backbones, then it’s possible for routing loops to develop between peer networks.
Q—what will happen to a datagram that is caught in a router loop?
A—it will circulate until its hop count goes to zero, then be discarded and an ICMP message sent to the sending host. Which one? Timeout.

## Slide 12: Today’s Internet
Each ISP operates as an autonomous system
ISPs meet at Internet Exchange Points, where they have peering agreements, connect directly
Traffic is exchanged without fee at IXP
IXPs have switches, ISPs run BGP through switches and through direct connections
More about autonomous systems later

## Slide 13: Today’s Internet
ISP
ISP
ISP
IXP
IXP

## Slide 14
Now on to routing…

## Slide 15: Automatic Route Propagation
Two separate protocols operate in routers
  Forwarding protocols—IP datagrams arrive, are forwarded
  Routing protocols—route information is shared with other routers
Routing protocols
  Compute shortest paths
  Respond to topology changes by updating shortest paths
Routing protocol software
  Runs independently of IP software, maintains FIB
  Occasionally updates forwarding tables used by IP

## Slide 16: Routing Algorithms
There are many (many many) variations on routing algorithms
They all fall into two categories:
  Distance-vector
  Link-State
Distance-vector
  Each router builds a list of destination networks and the next hop to reach destination in shortest number of hops
  Routers know nothing about network topology
Link-State
  Each router builds a map of the network topology
  Each router computes shortest path to each network
Why do you think each class of algorithm has the name that it does?

## Slide 17: Exchanging Route Information
How can routers exchange route information to keep routes up-to-date?
  Distance-vector (aka Bellman-Ford): routes are selected based on the distance between networks. Distance metric is something simple such as number of hops (routers) between them. Each router maintains a table of all networks in the internetwork and the number of hops to each.
  Shortest path first (aka link-state): selects routes based on a dynamic assessment of the shortest path between them. Each router maintains a map of the current topology of the network.

## Slide 18: Bellman-Ford Routing (Distance Vector)
Router keeps a list of destination networks, distance to each
Router sends copy of its router table to each router it reaches directly
The router table is a vector of distances
Notes: Figure shows initial router table. Router connects directly to two networks, each has distance zero.

## Slide 19: Updates
Marked entries cause changes to router table.
Router Table in Router K
Router J Update Message
Notes: This shows three cases of what happens when a new router table arrives.
Net 4: new table shows shorter route. Adopt new route.
Net 21: new table shows how to get to net 21, didn’t know how to get there. Add it.
Net 42: new table shows longer route to net 42, don’t adopt this new route
In a static environment, distance vector algorithm works well; but if routing information changes rapidly, propagation time of this method is too slow. Routes may never settle down, and some routers may have incorrect information.

## Slide 20: Disadvantages of Distance-Vector
Propagates slowly
  Can take multiple cycles for changes to propagate
  Messages exchanged tend to be large
Distributed computation of routes may not converge in presence of frequent changes
Doesn’t scale well

## Slide 21: Link-State (SPF) Routing
Called Shortest Path First—SPF
Each router table shows full network topology
  All routers
  Networks they connect to
Each router tests its neighbors
  Sends test message
  Propagates status of its neighbors
Router receiving message adjusts its topology table, uses Dijkstra shortest path algorithm to compute shortest path to each network

## Slide 22: Advantages of Link-State
Much less information is propagated
Scales better than distance-vector
Easy to identify and solve problems because of simplicity of information exchange
Each router computes its own routes, not dependent on possibly incomplete propagation of change information

## Slide 23: Link-State Example

## Slide 24: Heuristic Guideline
Up to 12 routers can participate in a single routing information protocol across a WAN
Up to 60 routers can participate in a single routing information protocol across a set of local LANs

## Slide 25: Autonomous Systems

## Slide 26: Autonomous Systems
Each organization’s networks are considered an autonomous system
Organization is required to keep router tables consistent, correct, in any way they please
One router from the AS is chosen as the router that will inform the outside world of routing within the AS
Notes: Note that original Internet core routers formed an autonomous system.

## Slide 27: Independent Autonomous Systems

## Slide 28: Border Gateway Protocol
ASs that exchange router information designate a router that will exchange information through BGP.
BGP machine is generally near the “edge” of the AS, called a border gateway or border router.
Notes: Current version is BGP-4.
In the figure, R1 and R2 are each gathering information about their networks and using BGP to send that information to the other.

## Slide 29: BGP
BGP shares next-hop information about the path from itself to another network
  This is shared with all external peers
  Also shared with internal peers
BGP does not share information about interior of its AS with other ASes

## Slide 30: BGP
Coordinates among multiple BGP speakers
Allows autonomous systems to communicate
Propagation of reachability information
Supplies next hop for each destination
Implements local policy decisions
Reliable transport (i.e., uses TCP)
Advertises path information to destinations
Incremental updates
CIDR address support
Authentication

## Slide 31: BGP Message Types

## Slide 32: BGP Message Header
Why does the header have a marker? What is its content?
Notes: Marker is agreed by both sides to mark the start of a message. All 1s in first message, later can contain authentication information. Contents must be agreed so that it can be used for synchronization.
LENGTH is the total message length, in octets.

## Slide 33: BGP Open
Notes: Two BGP peers each send OPEN message to declare AS number and establish other parameters. HOLD TIME is max time that can elapse between receipt of two successive messages. Version is protocol format, this is for version 4.
BGP identifier is IP address of sender.
Hold time is how long to wait between messages. Receiver is required to establish timer set at this value.

## Slide 34: BGP Update Message
Notes: Previously advertised destinations are withdrawn, and new destinations are advertised.

## Slide 35: Path Information
Notes: Not going to say much about this, except to note in passing that path information is provided. Can give path through several autonomous systems.

## Slide 36: BGP Reporting
R2 gives next-hop information to peers on behalf of the network
Notes: R1 is designated to speak BGP on behalf of he AS. It must report Net 1 as reachable through R1, and so on—reporting information from the perspective of the outsider, not a system inside the network.

## Slide 37: BGP Notification Message
BGP sends notification message, then closes TCP/IP connection
Notes: Errors are permanent—once detected, BGP sends notification, closes TCP connection.

## Slide 38: BGP Restriction
BGP does not advertise path lengths inside its AS
Because of this, BGP cannot choose shortest path
BGP is used to advertise only destinations that traffic can reach.

## Slide 39: Internet Routing Registry
Many registries exist
Shows which ISPs own which addresses
Allows validation that ISP advertising connectivity actually has that IP address
No centralized, authenticated registry
Routing problems exist
Notes: So ISP advertises reachability to route server using BGP. Good feature of BGP is ability to convey negative information, so that entries are dropped from tables.

## Slide 40: Summary
Must partition routers into groups, or information exchange would be burdensome
BGP is most used External Gateway Protocol
Each ISP is a separate AS, boundary at NAPs, where multiple ISPs interconnect

## Slide 41: Routing Within an AS
RIP
OSPF
HELLO

## Slide 42: IGP—Interior Gateway Protocol
Two ASs using their own IGPs internally, BGP between one another
Notes: A single router can use two different protocols simultaneously, one to communicate outside its AS and another to communicate within its AS.

## Slide 43: RIP—Routing Information Protocol
Routed—program that implements RIP
Participants are active and passive
  Active: advertise their routes to others
  Passive: listen to RIP messages, update router tables, but do not advertise
Update broadcast every 30 seconds
Update is pairs—network address, number of hops to it
Existing routes are kept until new route has lower cost
RIP routes time out in 180 seconds, are deleted
Notes: Q—does hop count allow for selection of optimal route in all cases?
A—No! Does not allow for difference of time on different networks
Final rule introduces hysteresis, prevents oscillation

## Slide 44: Slow Convergence Problem
Notes: In a, there is a connection to network 1. R2, R3 have learned the route to Network 1 from R1.
In b, that connection quits working or is disconnected; but R2 causes a routing loop by continuing to advertise it.
Now R1 will pick up R2’s advertised route to network 1. So packets from R3 to network 1 will come to R2 and then loop with R1, until hop count reaches zero.
Two routers can continue this forever.

## Slide 45: Solving the Slow Convergence Problem
Split horizon update—router does not propagate information about a route back over the same interface from which the route arrived
In example, R2 would not advertise a route to net 1 back to R1.
Hold down—routers ignore all information about a network for some hold down period after sending a destination unreachable message
Poison reverse—router immediately advertises infinite cost to reach removed connection
Notes: Broadcasting is very costly—RIP is inefficient.

## Slide 46: RIP1 Message Format

## Slide 47: Disadvantage of RIP Hop Counts
Low value for infinity restricts size of any internet using RIP
Restricts routing to hop-count metric; hop count may be poor predictor of delivery time
Routing becomes relatively static, unable to respond to changes in load

## Slide 48: HELLO
An IGP using a routing metric other than hop count (now obsolete)
HELLO
  Synchronizes clocks
  Allows each machine to compute shortest delay paths to destination
Allows machines to compute routes based on time

## Slide 49: Problems with Hello
Instability—protocols that change routes quickly can be unstable
Hold down is commonly used to increase stability
Time measurements are rounded

## Slide 50: Open SPF Routing
Interior gateway protocol using link state algorithm
Open, can be implemented at no cost
Includes type of service routing
Provides load balancing
Network partitioned into areas, separate from each other
Authentication for all router info exchanges
Notes: SPF—shortest path first

## Slide 51: OSPF Message Format
Notes: Version
1 hello (test of reachability)
2 database description (topology)
3 link status request
4 link status update
5 link status acknowledgement

## Slide 52: OSPF Database Description Message
Notes: Link type
1 router link
2 network link
3 summary link (IP network)
4 summary link (link to border router)
5 external link (link to another site)

## Slide 53: OSPF Link-Status Request Message

## Slide 54: OSPF Link-Status Update Message

## Slide 55: Summary
Manual maintenance of router tables is not practical for larger networks
An IGP (Interior Gateway Protocol) allows routers to exchange information
IGP implements either distance-vector or link state algorithm (SPF)